## Slide 1
GROUND SOURCE
GEOTHERMAL DRILLING
Harnessing Earth's Natural Energy for
Sustainable Heating & Cooling
RENEWABLE ENERGY · CLEAN TECHNOLOGY · EARTH'S CONSTANT HEAT

## Slide 2
What Is Ground Source Geothermal?
How It Works
Ground source geothermal drilling creates deep boreholes to install underground heat exchange loops that harness the Earth's natural thermal energy.
Unlike traditional HVAC systems that generate heat, geothermal heat pumps simply move it — drawing warmth from the stable subsurface in winter and expelling heat back into the cooler ground in summer.
The Earth maintains a consistent temperature of 50–60°F just a few feet below the surface, regardless of weather above ground — making it a reliable, year-round energy source.
50–60°F
Stable ground temp year-round
70%
Possible heating energy reduction
50%
Possible cooling energy reduction
50+ yrs
Ground loop lifespan
Source: U.S. Department of Energy

## Slide 3
Types of Ground Loop Systems
▼
Vertical Loop
100 – 400 ft deep
Boreholes drilled straight down using specialized rigs. Best for properties with limited land area. Most common in urban and suburban settings.
→
Horizontal Loop
4 – 6 ft deep
Pipes laid in wide, shallow trenches. Requires more land but is 20–30% cheaper than vertical drilling due to simpler equipment.
~
Pond / Lake Loop
Surface water body
Coils of pipe submerged in a nearby body of water. Very low installation cost but requires a sufficiently large, clean water source.
◎
Open Loop
Groundwater well
Uses actual groundwater as the heat exchange fluid. Highly efficient but subject to local water quality and permit regulations.

## Slide 4
The Drilling Process
01
Site Assessment
Geologists evaluate soil type, geology, available land, and heating/cooling load to design the optimal ground loop configuration.
02
Borehole Drilling
Specialized rotary or percussion rigs drill precision boreholes 150–400 ft deep (residential) or up to 3,000 ft for commercial installations.
03
Loop Installation
High-density polyethylene (HDPE) U-bend pipe loops are lowered into boreholes and connected into a closed circuit.
04
Grouting & Sealing
Boreholes are filled with thermally enhanced grout to maximize heat transfer and prevent surface water contamination.
05
Testing & Commissioning
The system is flushed with antifreeze solution, pressure-tested for leaks, and connected to the indoor heat pump unit.
From initial site visit to first use: typically 1–3 days for residential installations

## Slide 5
Benefits & Why It Matters
3–6×
CoP: heat output per unit of electricity consumed
75%
Max savings vs. conventional heating & cooling
$15K+
Typical installed cost for residential system
8–15
Years to payback through energy savings
Key Benefits
Reduces heating energy use by up to 70% vs. traditional furnaces
Ground loops last 50+ years with minimal maintenance
No outdoor units — hidden installation, minimal land footprint
Carbon-neutral when powered by renewable electricity
Qualifies for federal tax credits & utility incentives
Provides both heating AND cooling from a single system
Sources: U.S. Dept. of Energy · EnergySage · Geothermal Rising · Eaton Drilling & Pump Service